## Slide 1
CALIBRATION

## Slide 2: INTRODUCTION:
Sensor Fusion:
Sensor fusion is the ability to bring together inputs from multiple radars and cameras to form a single model or image of the environment around a vehicle.
The resulting model is more accurate because it balances the strengths of the different sensors.
Sensor Calibration:
It is the process where a sensor is adjusted, as accurately or error free as possible. With this , errors that occur through sensors are measured.

## Slide 3: OBJECTIVE:
Camera
Radar
LiDAR

## Slide 4: CAMERA CALIBRATION
Camera calibration mean the determining the internal and external parameters of the camera.
This transformation is usually divided into two parts:
Extrinsic and Intrinsic.
Intrinsic calibration estimates the internal or intrinsic parameters of a sensor, e.g., focal lengths of a vision camera, which correct for systematic or deterministic aberrations (errors).
The intrinsic parameters of a camera depend on how it captures the images. Parameters such as focal length, aperture, field-of-view, resolution, etc govern the intrinsic matrix of a camera model.

## Slide 5
The extrinsic parameters of a camera depend on its location and orientation and have nothing to do with its internal parameters such as focal length, the field of view, etc.
The extrinsic parameters are transformation matrices that convert points from one coordinate system to the other
The extrinsic matrix is a transformation matrix from the world coordinate system to the camera coordinate system, while the intrinsic matrix is a transformation matrix that converts points from the camera coordinate system to the pixel coordinate system.
So in order to construct the matrix from the image we need two things Position and orientation of the camera

## Slide 6: RADAR
The radar calibration is a method which allows to scale unknown signals by means of standardized signals.
Radar investigations are aimed to quantify radar echoes for studying target properties, there is a need to calibrate such systems.
Absolute calibration capability is necessary for conventional radars as well as for SAR systems

## Slide 7: FUTURE PLAN:

## Slide 8: REFERENCES:

## Slide 9: THANK YOU